## Slide 1
Safety Critical Communications
MODULE FOUR:
PROTOCOLS 2

## Slide 2
Briefer’s Introduction:
Welcome to the fourth module in our course on safety critical communications. Here we return to the subject of ‘protocols.’
This module looks at the following:
Intro – a reminder of what SCC is and why it is important
Standard words and phrases
The Emergency Call
The effect of communications equipment

## Slide 3
How the Course Works:
The programme consists of six modules. We recommend that they are delivered in order, but you may select a particular module if required:
Foundation
Protocols 1
Structure and Lead Responsibility
Protocols 2
Confirming Understanding
Communication Skills
*Please read the Briefing Notes prior to delivering a module. They provide background information to enable you to manage the exercises and discussions.
*You will also be required to perform a short assessment at the end of the course to make sure attendees understand the content. See the Briefing Notes.

## Slide 4
Welcome

## Slide 5
Safety Critical Communications

## Slide 6
Protocol: an agreed way of doing something
VO

## Slide 7
VO

## Slide 8
ABC- P
A
ccurate
B
rief
C
lear
P
rofessional
VO…

## Slide 9
VO

## Slide 10
“zero two zero… three one four two… five three zero zero”
“twenty-four miles”
“zero nine hundred hours”
VO…

## Slide 11
Standard words and phrases
Emergency call
Effect of equipment
VO

## Slide 12
Standard
National
MINIMUM
Note, there will be a short test at the end of this module to confirm your understanding of the National Minimum Standard.
VO…

## Slide 13
Standard Words and Phrases

## Slide 14
Q. Why do we have standard words and phrases?
Q. Which ones can you remember?
VO

## Slide 15
…VO

## Slide 16
“Safe to go?”
“Go / No”
VO…

## Slide 17
NOT CLEAR
VO

## Slide 18
VO…

## Slide 19
List of standard words and phrases:
Phrases to use when using a radio or telephone
Correction
I have made a mistake and will now correct the word or phrase just said.
Repeat back
Repeat the message back to me.
Other phrases to use when using a radio and only one person can be heard at a time
Over
I have finished my message and am expecting a reply.
Out
I have finished my message no reply is expected
This is an emergency call
This message provides information which needs immediate action to prevent death, serious injury or damage.
VO

## Slide 20
“You now have my authority to pass mike echo two three signal at danger. Proceed at caution as far as mike echo two five signal.”
VO

## Slide 21
“Make no further movements…..”
“Await signal…..”
“Obey all other signals.”
“When I give you permission….”
“Proceed at caution.”
On the approach to…. And beyond…..
Here are some more phrases that a Signaller may use:
Skip this section
VO

## Slide 22
“What I require you to do driver…….”
“Make a wrong direction movement from………. to…………”
“Proceed up to.….”
“Stay in a position of safety..…”
“You now have my authority to…….”
Here are some more phrases that a Signaller may use:
VO

## Slide 23
“Obey signal….”
“Report your findings at/to……..”
“The line is now clear and safe for trains to run on.”
“The …. Line is blocked”
Here are some more phrases that a Signaller may use:

## Slide 24
Here are some more phrases that a Signaller may use:
“Driver, I’m detaining you at……signal because of……….. (give a reason)
Or
When authorised, I require you to pass……… signal at danger.
Proceed at caution through the signal section / as far as ……….ONLY.
VO

## Slide 25
Correction

## Slide 26
CORRECTION
use when correcting our own verbal mistake
VO…

## Slide 27
What effect does the Signaller’s
mistake have on the message Opening?
This example, and the one on the next page, are both taken from recorded communications.
Example
Model
Answer
VO

## Slide 28
Which version is more ‘ABC-P?’
Note, these may sound strange if you are unfamiliar with shunt moves. The communication takes place over a radio in a yard. Tracks in yards and depots are called ‘roads’ and these are given names such as ‘stables’ or numbers such as ‘six road.’
Example
Model
Answer
VO

## Slide 29
Say ‘CORRECTION’ and then
RESTATE THE MESSAGE CORRECTLY
VO

## Slide 30
Repeat Back

## Slide 31
Repeat the message
back to me
REPEAT BACK
VO

## Slide 32
Opening
Actions
Information
Confirmation
“Repeat Back”
VO

## Slide 33
Opening
Actions
Information
Confirmation
Note, the ‘repeat back’ in the Confirmation should focus on the agreed actions.
“Repeat Back”
VO

## Slide 34
Use the standard words and phrases:
a) using a radio or telephone
b) using a radio and only one person can be heard at a time
Correction
Repeat Back
This is an emergency call
Over
Out
VO

## Slide 35
Making an Emergency Call

## Slide 36
This is an emergency call
VO…

## Slide 37
Opening
Actions
Information
Confirmation
VO

## Slide 38
“This is an emergency call”
“My name is…”
“I am a…”
“I work for…”
“I am standing at…”
“I require (which emergency services…)
It is important to give this information first, in case contact is lost.
VO

## Slide 39
…VO
.
.
.

## Slide 40
Opening
Concise Information

## Slide 42
Opening
<Pause>
Concise Information
Pause for a couple of seconds to form a coherent message.
VO…

## Slide 43
…

## Slide 44
Opening
<Pause>
Concise Information
Actions
Confirmation
VO…VO

## Slide 45
…

## Slide 46
Mini Workshop
Split into groups.
Each group should write a realistic emergency scenario, relevant to their job function.
One member of each group should make the emergency call while the rest listen in.
Whilst it is stressful to make a call in front of your peers it is more stressful to make an emergency call in a real emergency situation.

## Slide 47
Learn to make an Emergency Call
It is important to practice making an emergency call on a regular basis
VO

## Slide 48
Communication Equipment

## Slide 49
Technical note: simplex, sometimes called ‘half duplex’ or ‘press to talk,’ allows communication in one direction at a time.
Duplex allows simultaneous communication in two directions, like a mobile phone.
Multiplex supports many-to-many communication, like a conference call.
Note on Emergency Call:
Emergency calls made using the GSM-R system red button are simplex – ‘press to talk.’ This is different to normal operation. Make sure it doesn’t catch you out.
VO

## Slide 50
Improved Reception
Specific Emergency Call feature
Caller Identification
Full duplex operation
VO

## Slide 51
In what manner are the participants talking to each other?
Specifically, what is happening?
What happens as a result?
The hand signaller is standing track-side, talking on a GSM-R radio.
VO

## Slide 52
What effect has the ‘press to talk’ equipment had? (think ABC-P)
VO

## Slide 53
…VO

## Slide 54
Safety Critical Communications is a formal conversation.
VO

## Slide 55
Module Review
VO

## Slide 56
1
Use the standard words and phrases
2
Learn and practice to make an Emergency Call
3
Safety Critical Communications are a formal conversation
VO

## Slide 57
Module Conclusion
VO

## Slide 58
VO…

## Slide 59
Your briefer will now conduct a short test to confirm understanding.
Every time we hold an operational conversation, we are agreeing a contract
- keep the contract tight
VO