## Slide 1: Lifting Group Report
Malcolm Miles

## Slide 2: Group Members
Jim Nabarro Balfour Beatty Rail
John Ockenden Carillion
Nick Powell Colas Rail
Ian Pollard Amey Colas
Darren Matthews Readypower
Stephan Williams Road Rail Cranes
Steve Shields Volker Rail
Bill Meyers London Underground
AND
John Watson

## Slide 3: COP 8 – Tandem Lifting with Two Excavator Cranes
Issue 6 Published August 2015
Incorporates guidance from former TLWG that was available through Safety Central
  Scope includes construction based and rail conversion excavator cranes
  Lift Planners should use Tandem Lift Duty Charts
  When using single lift duty charts SWL should not be less than calculated load share plus 50% - also applies to rating of lifting accessories
  Crane controller responsibilities
  What to do in the event of a motion cut

## Slide 4: COP 11 – Planning for lifting Operations
Issue 4 Published August 2015
  Lift Planner Competence defined
  Planning to 90% of crane duty
  More guidance on when to use maximum and minimum duty charts
  Guidance on de-rating of lifting accessories
  Impact of wind speeds
  Potential to oversail onto third party premises
  Reference to COP032 (ALO)
  Sample site Survey checklist added

## Slide 5: Poster L1 – RCI Motion Cut
Published November 2015
  What it is
  What action to be taken by the Crane Controller and Operator in the event of Motion Cut

## Slide 6: Poster L2 – Tandem Lift Duty
Published March 2016
  Reinforces planning controls in COP008

## Slide 7: Poster L3 – Crane Controller Competence for Twin Jib Cranes
Published July 2015
  Crane Controller (OTM-TRM)
  Competence – classed as single lift – tandem lift competence not required

## Slide 8: Poster L4 – Lift & Carry in Road Mode
Published April 2016
  RCI has single road duty which assumes flat and level ground
  Need to consider down rating when not on flat and level ground

## Slide 9: Poster L6 – Lifting Accessory Misuse
Published January 2016
Published in Conjunction with Plant Sub Group
  Guidance on correct use of lifting accessories

## Slide 10: Current Workstreams
  Standardised Lift Plan Template
  Review of BS 7121:2016
  Poster on Mechanical MLD’s
  Review of COP030