## Slide 1: 12th M&EE Group Plenary Meeting 15 June 2016
Plant Sub-Group
Notes: <number>

## Slide 2: Current Membership
John Ockenden Carillion Rail Chair
Jim Nutty Amey
Neil Halliday RSSB
Steve Wadham Total Rail Solutions
Peter Stone Network Rail
Jim Nabarro Balfour Beatty Rail
John Rose London Underground
Ian Lawson King
Dave Turner/Sam Snelson TXM Plant
Notes: <number>

## Slide 3: Plant Sub Group COPs updated since last year
COP015 issue 4 – Load lifting points on RR Excavator Cranes
COP0021 issue 4 – Safe use of Quick Hitches
COP024 issue 5 – Use and Loading of MEWPs
Poster P4 - RRV braking
Poster P7 - MEWP planning
Poster P8 – Freezing Fire Extinguishers
RPA fitter competence
Notes: <number>
COP15
Non calibrated lifting points to be blanked off because all machines should be certified to 1530 whch has always required all load lifting points to be calibrated. Colour of load lifting points added (Red)
Cop21
Guidance on Semi-automatic QH “Should Not Be Used”. New paragraphs added 1.3.2 semi-automatic quick hitch use, 3.2 on adaptor plate inspections and 3.5, concerning removing accessories
COP24
Full review with update sections on emergency recovery and unsafe use of MEWPs Manipulating OLE not good practice, Emergency planning and rescue added
P7
P4 RRV braking no big changes, there was talks about removing the non service braked towed load but left in as it shows what could happen if its not connected up

## Slide 4: Plant Sub Group New since last year
COP032 – Any Line Open (ALO) working
COP035 – Plant modules on Wagons/ trailers
Poster P9 - misuse of MEWPs
Strapping down of plant design requirements
Notes: <number>
COP 35
Is about completing and Engineering change assessment
The Professional Head of Engineering should determine whether
equipment fitted to rail wagons or trailers are considered as a load or
a plant module.
Fixed or removable equipment capable of being attached
to a rail wagon or trailer, performing a specific function
whilst wagon or trailer mounted.
Requirement:
To transport OTP safely, suitable and sufficient tie down points or securing system to anchor the OTP shall be provided and clearly identified. Instructions for their use shall be included in the operations manual.
Guidance:
A review of the existing tie down points should be carried out to ensure that the tie down points and securing equipment to be used will not foul/damage any of the rail equipment added during conversion.
Where existing tie down points are found to be unsuitable then these should be blanked off/ removed/ disabled.
Where necessary new tie down point should be fitted and labelled in accordance with ISO 6405-1 2004 symbol 7.27

## Slide 5: Plant Sub Group Reviewed with no change
All Cops and posters reviewed in accordance with the plan
COP 0022 – Dragging rail with RRV cranes
COP 0023 – inspection of demountable MEWSPs and lifting equipment
Notes: <number>

## Slide 6: Plant Sub Group Currently working on
AP001– Audit protocol for hire of RRVs
COP 007 – On Off tracking Definition of secured timbers
COP 025 – Brake testing of RRVs Trailers and hydrostatic drive machines
COP 033 – Gaining assurance when procuring OTP services
COP 034 – On Track Piling
Poster on exclusion zones
COP032 ALO
Inadvertent movement of excavator cranes
Earth bonding of RRVs
Notes: AP001 aligning with the current RISQS protocol
COP 024 and both posters being reviewed with emergency recovery and misuse of MEWPs
<number>