## Slide 1
Proximity Warning Systems:
For On-track Plant
Exclusion Zone Enforcement
Chris Browne – Senior Engineer, Rail Innovation Development Centre - Melton

## Slide 2: Exclusion Zone Infringement!
Incident examples:
Hither Green 2011 – employee crushed between lorry and RRV
RRV traps operative against Hope station platform – 8 March 2013
Worker Crushed to Death by Slewing Plant tunnelling 21/10/2013
Man’s foot crushed by RRV excavator 2015
In the last 10 years there have been 430 accidents involving machinery, 43 of these were major RIDDORs and 4 were fatalities (Network Rail 2015).

## Slide 3: Regulatory Obligations
Employers have an obligation to protect workers where:-
‘… a person may be endangered by the movement of a vehicle, suitable and sufficient steps to give warning to any person who is liable to be at risk from the movement of the vehicle’, as well as the general duty to provide safe access and egress under Regulation 17
Regulation 28 of Construction Design and Management Regulations 2015

## Slide 4: Current Warning Controls
1) Life Saving Rules
Strengths -Standardised high level requirements
Weaknesses -Doesn’t provide a method of warning
2) Sounding warning horns/buzzers before moving
Strengths -Provides a method of warning
Weaknesses -Operator dependent; it can be forgotten
-Not enough warning time to move out of danger
-Doesn’t provide a method of recording data
-Doesn’t provide a method of redress
-Doesn’t drive positive cultural habits – reliance on horn
3) Machine Controller
Strengths -Potential method of staff redress
Weaknesses -Impaired visibility
-Many things to concentrate on at once
-Multiple pressures and hindrances limiting ability to redress effectively
-Inconsistent impact to cultural enhancement

## Slide 5: Proximity Warning System benefits
PWS is designed to support the safe management of Exclusion Zones achieved through processes such as:-
  Alert Intruder of the incursion directly
  Alert Machine Operator of an incursion* (Preferred systems)
  Alert Machine Controller of an incursion* (Preferred systems)
  Record of the event to enable redress and continuous safety monitoring* (Preferred systems)
Whilst they are not a preventative they do benefit and enable both:
  Provide emergency warning, enabling Machine Operators to stop all movements
  Drive cultural change and behavioural monitoring through data collection* (Preferred systems)
* Not all systems log an incursion or activate a localised warning – preferred systems do both these

## Slide 6: How does it work?
A PWS system (generally modular) is mounted on the Plant asset
The local work force is issued with and wears a corresponding radio tag (with unique ID reference)
The PWS system then activates when the tag comes within a predefined distance of the machine
4. The tag then either:-
  Activates and warns the wearer (usually through vibration)
  and/or sends a signal back to the mounted PWS system, logging the intrusion and providing both visual and audible warning to the M/O, M/C and the local working party* (Preferred systems)
The Machine Operator stops all movements!

## Slide 7: Different PWS Systems
Different System designs provide different levels of functionality.
Fitment: Can be fixed (integrated in the machine or retro fitted as a modular solution)
Telemetry: Data logging can provide specific details about the event i.e. camera footage or provide remote data interrogation
Null Zones: Enabling some pre planned interventions either through variable quadrant selection, activation ranges or direct M/O nulling
Tag types: Passive, Active or Semi-Active options with Vibrating or non-vibrating functionality

## Slide 8: Cross Industry PWS Use
PWS is widely used throughout other industry e.g.
Mining (particularly in quarries and Open cast)
Ware housing
Construction sites
Aviation

## Slide 9: PWS Product Acceptance PWS systems are subject to Network Rail’s Product Approval process!
Time line | Applicant | Existing Application and trial Progress
2009 | NR SIP | Early Trials held at RIDC Tuxford (later added to RRV Safety Improvement Programme)
2014 | NR IP | MyZone Product Acceptance as a base solution via IP team
2015 | BB Rail and Carillion (Cross Rail) | Working group implemented stakeholder HAZID events SiteZone Limited Trial Acceptance (all lines closed, primarily allowing off track operation for Behavioural study and Interference assessment)
2015-2016 | BB Rail and Carillion (Cross Rail) | Product Acceptance closed out of open HAZID entries (independent interference and coexistence review (Affini) and Behavioural studies (in partnership with Notts Uni)
March 2016 | BB Rail and Carillion (Cross Rail) | SiteZone Trial Acceptance reissued (Live trials)

## Slide 10: Key learning from PA review
HAZID
These system bolster current risk controls, the benefits of this system are primarily realised through cultural change (prevention) and as a last line of defence and in support of current controls – i.e. life saving rules.
Interference and Coexistence Study
Likely hood of critical interference (at 125Khz and 868Mhz) between PWS and other critical infrastructure RFID was determined to be low risk in terms of corporate risk
Behavioural Studies
The current methods of working don’t generally support good practice when considering exclusion zone management e.g.
  limited clearance for workforces to pass machines,
  limited reporting of intrusion,
  reliance on the M/C to manage intrusions,
  lack of available/reliable data

## Slide 11: Ongoing Trials – Cross Rail (BB Rail and Carillion)
Trials will be used to refine:-
Installation management processes – different machines, different fitment methods; when to fit, how to fit, Tag allocation management
Worksite controls – How do workforce pass machines, ‘permissible’ access for roles such as Crane Controllers and slingers
Data management – review how data can be managed and used to reinforce Life Saving Rules (enhance close call reporting, staff retraining and redress etc.)

## Slide 12: Objectives (If trials are successful)
Short term Goal:
  Approval of ‘preferred’ PWS system types for use throughout NR infrastructure
Longer term aspirations:
  National application guide/specification
  Enhanced technology Introduction
  Mandate or recommend for certain work activities
  Permanent Integration into OTP

## Slide 13: Questions