## Slide 1
Advances in Collision Avoidance, Proximity Detection & Exclusion Zones
June 2016
Jason Stout
Vice President
Phil Banfield
Senior Electrical Engineer
Approved Service Partner for The PBE Group

## Slide 2: Agenda
The Vision- A complete solution to provide proximity awareness
Technologies - What is the right technology?
Reporting - The capability of a system is measured on the data is provides
The Sales Bit….. PBE’s Proximity Alerting System (PAS) portfolio
Rollout Considerations Direct purchasing, rental, leasing and plant hire solutions
Who we are - The PBE Group and SES Group overview.

## Slide 3: The Vision A complete solution to provide proximity awareness
Provide proximity awareness and collision avoidance for personnel, machines, vehicles and danger zones
Examples of usage:
  Prevent collision between vehicle and personnel/vehicle
  Create safety zones around dangerous machinery
  Create exclusion zone for hazardous areas
Entry control and tracking
  Tracking of all personnel, machines and assets
  Entry and exit control on sites
  Electronic tally boards
A single monitoring and control software solution
Vehicle/Loco safety zones
Vehicle proximity awareness
Hazardous area protection zones
Dangerous working areas
Personnel tracking
Centralized control and monitoring of personnel and assets/vehicles

## Slide 4: Technologies Which is the right technology?
Multiple technologies have been used for collision avoidance such as banks man, RFID, reversing cameras, heat sensing technology, electromagnetics, pulse radar, bi-directional radar, GPS etc.
All technologies have restrictions but a combination can provide accuracy, range and direction
 | Range | Accuracy | Notes
RFID | ≈ 60m, 200ft | Zonal awareness | Accuracy limited, can be configured to cover a small area protection with average range
Bi-Directional Radar (Tag) | ≈ 100m, 300ft | ≈ 0.3m, 1ft | Requires partial line of sight
Cameras | N/A | N/A | Requires driver interactions, informative only
Pulsed radar (Non Tag) | ≈ 5m, 15ft | ≈ 0.3m, 1ft | Detects everything, good for car reversing and requires line of sight
Electromagnetics | ≈ 10m, 30ft | ≈ 0.3m, 1ft | None line of sight
GPS | Autonomous 2.5 m ( ≈ 8.2 ft) CEP; SBAS = 2.0 m ( ≈ 6.56 ft.) CEP |  | 

## Slide 5: Reporting The capability of a system is measured on the data is provides
Every event needs to be recorded, so that can be replayed in real time or through reports
Flexible analysis e.g. incidents per shift, danger zone analysis, vehicle monitoring, individual worker etc.
Predictive - identifies safety issues thus allowing training to increase safety, before an accident happens
Outputs:
  Easy to use and flexible
  Simplistic graphs and charts
Simplistic operation
Multiple display type
Tracking

## Slide 6: The Sales Bit….. PBE’s Proximity Alerting System (PAS) Portfolio
PAS ZR PAS Z
MiniTAG Obstacle Tag Tag Charging Station
PAS C
Multiple technologies (EM, GPS, Bi-Directional Radar and RFID)
User definable ranges (Urgent, Mid and Far)
Customizable audio and visual warnings
Advanced monitoring and reporting systems, Wi-Fi compatible
Geo-fencing capability
4 outputs and 4 inputs alarms allowing optional control and interaction with vehicle and machines
Recognizes 4 user definable groups, such as personnel, assets, vehicle types, visitors, obstacles etc.
Critical reports for daily review and full data capture for offsite analysis
Compatible with PBE’s tracking system and entry/exit system functionality for an integrated solution

## Slide 7: Rollout Considerations Direct purchasing, rental, leasing and plant hire solutions
PBE offer leasing and rental options through an affiliated entity as an alternative to CAPEX cost
The solution is modular, providing a cost effective solution for all applications and vehicle types
PBE design, manufactures and supports it’s own products – enabling the most advanced and sophisticated portfolio at a very competitive cost
Complete solution from supply, installs to system management
Software Menus
Accessible data

## Slide 8: Who we are? A global manufacturer of safety and productivity solutions & world class service provider
PBE have been a leading manufacturer of safety, monitoring and communications equipment for 45 years
170 employees, 9 regional service centers and over 30 distributors
With an estimated 850 tunnels and mines, served by Over 70 proprietary products – all designed and manufactured in house to form a total integrated solution
PDS - Environmental Monitoring - Conveyor Belt Monitoring - Leaky Feeder Solutions -
Tagging & Tracking - Complete Mine-wide Software Solutions
Provide services to Tunnelling, Civil Engineering and Rail Industries
400 employees with offices throughout the UK
Privately owned, founded in 1998
Experienced and highly skilled and qualified workforce
UK market leader in the Engineering sector

## Slide 9: Thank You
Jason Stout
Vice President - Europe, Middle East and Africa
PBE European Headquarters
Milton Keynes
United Kingdom
jstout@pbegrp.com
Tel: 07765 523230

## Slide 10: Additional Slides for reference only – None presentation

## Slide 11: PAS Z & ZR Overview Benefits of the PAS System
The PAS Z is a cost effective tag based solution for above & below ground – the ZR is a ruggedized version
Suitable for mines, worksites, depots, temporary possessions and hazardous areas
Accurate range and direction for all vehicles, personnel, obstacles and assets
Audio and visual warnings with the option of an external strobe/siren
All events logged internally with an extensive reporting capability
Simplistic local configuration or user friendly software for future download
Wi-Fi enabled to allow remote monitoring and configuration
Self-contained for simplistic and quick installation

## Slide 12: PAS Z & ZR Features Overview of the features
Multiple technologies for redundancy and accuracy
User definable ranges (Urgent, Mid and Far)
Customizable audio and visual warnings
Advanced monitoring and reporting systems
Geo-fencing capability
4 outputs and 4 inputs alarms allowing optional control and interaction with vehicle and machines
Recognizes 4 user definable groups, such as personnel, assets, vehicle types, visitors, obstacles etc.
Critical reports for daily review and full data capture for offsite analysis
Compatible with PBE’s tracking system and entry/exit system functionality for an integrated solution
Powered via the ignition circuit of the vehicle/machine or via an auxiliary power source

## Slide 13: Technologies Used 4 technologies to provide redundancy and accuracy over long distances
Multiple detection technologies - EM (Electromagnetics), RFID, GPS & bi-directional Radar
GPS receiver for surface tracking and defining site geo-fencing
Magnetic solid state compass
Wi-Fi enabled
USB port for configuration and data extraction without wireless connectivity
FREQUENCIES |  |  | 
 | ITU Region 1 (EMEA) | ITU Region 2 (Americas) | ITU Region 3 (Asia/Oceania)
RFID | 868.3MHz | 915MHz | 920MHz
Radar | 4.5GHz | 4.5GHz | 6.5GHz
Electromagnetic (EM) | 122.1kHz | 122.1kHz | 122.1kHz

## Slide 14: PAS Technology Overview Combining 4 technologies to provide all range protection and redundancy
All technologies have restrictions but a combination can provide accuracy, range and direction
PAS uses the most accurate of the combined technologies, dependent on vehicle type, application or requirement
Precedence for each technology can be defined
RANGE & ACCURACY ESTIMATIONS |  |  | 
 | Range | Accuracy | Notes
RFID | ≈ 60m, 200ft | Zonal awareness | Accuracy limited, communications channel only for EM and GPS. External antenna optional
Radar | ≈ 100m, 300ft | ≈ 0.3m, 1ft | Requires partial line of sight, external antenna available as an option
Electromagnetic | ≈ 10m, 30ft | ≈ 0.3m, 1ft | None line of sight
GPS | Autonomous 2.5 m ( ≈ 8.2 ft) CEP; SBAS = 2.0 m ( ≈ 6.56 ft.) CEP |  | 

## Slide 15: General Specifications High level specifications for the PAS Z & ZR
GENERAL SPECIFICATION | 
PAS Z Enclosure Dimensions | 6.014(L) x 4.008(W) x 1.502(D) inches
 | 152.8(L) x 101.8(W) x 38.2(D) millimeters
PAS ZR Enclosure Dimensions | 6.14 (L) x 4.95 (W) x 4.45 (D) inches
 | 155.96 (L) x 125.73 (W) x 113.03 (D) millimeters
Input & Ignition Voltage | 11-15 VDC (Optional 24-12VDC convertor available)
Temperature | 0˚to 70˚C ¦ 32˚F to 158˚F
Outputs (4) | Dry relay contacts for outputs 1, 2 and 4. Relay 3 reserved for strobe/siren functionality with its own 12VDC supply (internally fused)
Inputs (4) | Input 1 & 2 External Sense (Up to 30VDC) 0-1.2V = 0, >3.3V = 1 Input 3 & 4 Internal Sense (Dry Relay Contracts compatible) NO = 0, NC =1
Internal Storage Capacity | 25GB
Warranty | 12 Month

## Slide 16: PAS Z Unit Compact solution designed for in vehicle/cab use
Designed for in-cab mounting
Powered via a 12VDC source (either via the ignition circuit or auxiliary power source)
Built in RFID, Radar & GPS as standard, up to 4 EM Sensors optional

## Slide 17: PAS Z Connections Compact unit for quick deployment
(i.e. Optional sounder/ Strobe or Creep & Brake functionality)

## Slide 18: PAS ZR Ruggedized Unit IP65 unit for external mounting
Same functionality as the PAS Z but contained within a ruggedized box and external connectors
Can be mounted within the cab if extra protection required or external to the cab

## Slide 19: PAS Z Connections Compact unit for quick deployment

## Slide 20: Display Operation How range and direction is shown
Distance to the closest object is displayed
The total number of each object type is indicated in the 4 counters, showing how many of that object in each of the 3 zones
Radial lines of LEDs emanating from the center indicate the angle of detected tagged objects
Bearing is achievable by EM, Radar and GPS – if no bearing is available the circle will provide zone indication
A sensor will provide automatic dimming in bright conditions
The arrows allow for complete local configuration of the system and fault finding
PAS Display

## Slide 21: PAS MiniTags and Notifications Personnel tag functionality
Personnel tag contains all 4 technologies
Same tag used in PBE’s tracking solution
LED performance indicators
Power indicator
Sounder and LED indication when within a set distance of vehicle
25, 10 and single charging stations available – acts as a tally board
Tag test stations available
 | RFID | EM | GPS | RADAR
RED | Attached to PAS-110 Lightbar | Invalid EM reception | On but no fixed GPS position | Radar out of range
GREEN | Attachment to Lightbar pending user acknowledgement | Valid EM reception | GPS position fixed | 2 way comms tag & PAS – System OK
BLUE | RFID packet transmitting | EM packet transmitting | GPS packet transmitting | The tag recognizes a PAS system but the PAS system is not picking up the tag
MiniTAG LED Indications Tag Charging Station
LED Indications

## Slide 22: Cap Lamp Tag and PAS-O Convenient tag inserted into the cap lamp assembly and additional Obstacle tag
Cap Lamp Tag:
  Tag designed to be inserted into existing cap lamp (or provided as new)
  Power taken from the cap lamp battery
  Optional AVA available, that will provide an audible and visual indication for the user
Obstacle Tag:
  Same as Tag functionality, but in a robust enclosure
  Used for locating assets/obstacles/machines or providing to visiting vehicles
  Provides the users of the PAS system warning to the assets/obstacles/machines
  Clear indications on the front panel
  Charged via a USB port
Obstacle Tag
Cap lamp Assembly with AVA

## Slide 23: Configuration, Control & Monitoring
The PAS Z & ZR have software to allow configuration, control and monitoring­
The information can be transferred to the PAS unit via a USB stick or via Wi-Fi connectivity
Each unit has a configuration file that can be stored or changed off-line for later download
Reports are also accessed via the software
Software Menus
Accessible data

## Slide 24: Configuration – Set Up General vehicle and warning set up
Adjustable volume control
Set the vehicle dimensions
Drag and drop sensor positioning, EM and GPS
Each of the 3 zones can be independently set for each tag group
Different alerts for the 4 different tag groups
Different alerts for the 4 different tag groups

## Slide 25: Configuration – Set Up Further configuration options
Linked tags allows certain tags to be non-alarming, however still monitored
Controls the display types and user preferences
Geo Fencing for hazardous areas, will alarm is vehicle or machines enters or leaves zone
Set the compass (required for GPS positioning)
System menu provides additional configurable screen, including reports and config. export
Control of the input and output digital relays

## Slide 26: Additional Functional Linking & attachments
 | Linking | Attachment
Suppresses Audible Warnings | Yes | Yes
Suppresses Visual Warnings | Yes | Yes
Global or Local Feature | Local | Global
Suppression Intended For | External Objects | Occupants
Remembered Across Power Cycles | No | No
Attachments
  RF Bubble is set up around the PAS equipment (approx. 1m max)
  The driver “attaches” his tag to the vehicle by pressing the tag button twice
  No alarm will be generated by that machine for that tag (activity still recorded)
  The driver will then not set off other vehicle alarms because he is attached to that vehicle
Linking
  The PAS system can be linked to single or multiple tags (pre defined via the software)
  Typical use is when one vehicle loading another or banks man
  Performed when TAG is in the urgent zone
  Driver links tags by tapping on the top of the PAS Z & ZR

## Slide 27: PAS On-Site Testing Stations In field testing stations for tags and vehicle units
Independent units to provide on site verification of system performance
This is in addition to the PAS system having an internal start up procedure and fault diagnosis
The TAG Testing Station verifies all tag technologies are fully functional
  Tag presented within approx. 0.5m
  Simplistic Green Pass/Red Fail indication
Vehicle Testing Station provides:
  After initial commissioning records Vehicle ID, Number of Sensors, Technologies
  Vehicle passes close to check station for verification vs. past configuration
  Simplistic Green Pass/Red Fail indication

## Slide 28: Wi-Fi Capability Simplistic data retrieval and configuration uploads
Wi-Fi provides a convenient way of uploading new configurations or downloading data from the vehicle for analysis via the reporting software
Local Wi-Fi access points are established that will allow for constant downloading of data to a computer located in the service hut
If the service hut has LAN /WAN connectivity, then the data can be accessed externally for remote evaluation
This can also be achieved using reliable 3G/4G connectivity

## Slide 29: PAS C Solution for large vehicles/machines
Accurate provision of range accuracy and direction to all PAS LV, PAS LV-Z and personnel
RFID, GPS and 2-6* EM sensors (*depending on vehicle size)
In addition to the functionality of the PAS Z & ZR, the PAS C offers:
  Radar type representation of all vehicles, people and assets
  Programming on the computer display
  Interactive display
            Full local on site reporting (can be downloaded for external review)
            Optional cameras