## Slide 1: Rule Book Updates December 2018
An overview of the changes affecting workforce

## Slide 2: Where to find the changes?
Briefing leaflet:
https://www.rssb.co.uk/rgs/rulebooks/GERT8000-RBBL%20Iss%2032.pdf
Presentations & videos: will work only on I-phones/pads or those with access to YouTube
https://www.rssb.co.uk/Pages/Standards-Update.aspx

## Slide 3: Changes that affect workforce
Handbook 8 IWA, COSS or PC blocking a line & Handbook 21 Safe work leader (SWL) blocking a line
A line blockage can only be granted with a train within the portion of line concerned either where this is authorised, or when the train has become disabled and the driver has told the signaller it will not be moved.
Additional protection should always be used when it is possible to do so, as shown on the revised Line Blockage Form (NR3180).
To clarify the intended meaning, the wording of section 5.1 has been changed to state that the request to the signaller to restore a disconnection of signalling apparatus must not be made until after the line blockage has been given up or suspended.

## Slide 4: Changes that affect workforce
Handbook 16 AC electrified lines
Because of the introduction of bi-mode trains which can either operate as electric trains drawing power from the ac electrification system, or in a self-powered mode using their own tractive power, a number of changes have been made to the rules in this module. Bi-mode trains change over between self-powered and electricmode at planned locations, and may also do so in order to travel into areas where there is damage to the overhead line equipment.
Section 3.1 has been changed to make it clear what is meant by overhead line equipment (OLE) being made safe, and that the OLE must still be treated as dangerous.
Section 7 has been changed to state that the electricity must always be switched off before a person above or near to the OLE is approached.

## Slide 5: Other changes
Glossary - Glossary of Railway Terminology
Handbook 16 AC electrified lines
Module AC AC electrified lines
Module M1 Dealing with a train accident or train evacuation
Module M2 Train stopped by train failure
Module S5 Passing a signal at danger or an end of authority (EoA) without a
movement authority (MA)
Module SS1 Station duties and train dispatch
Module TS1 General signalling regulations
Module TS2 Track circuit block regulations
Module TS10 ERTMS level 2 train signalling regulations
Module TW5 Preparation and movement of trains: Defective or isolated vehicles and on-train equipment
RS521 Signals, Handsignals, Indicators and Signs Handbook

## Slide 6: Questions?