## Slide 1: Clapham- learning from history: Appendix a- Lessons from other significant passenger accidents

## Slide 2: Appendix slides
Sadly Clapham was only one of many significant passenger accidents from1980’s into the early 2000’s.
Each of these accidents led to changes in the way we work, changes to rules or standards.
Please choose one or two that your audience would relate to and discuss. Choice can be influenced by your location, skill set of your audience, or even job roles.
Lessons include failure of maintenance regimes, communication breakdowns, rule violations and cultural issues.
On your chosen accident(s) please discuss what we do differently now, and do we still put into practice improvements to process, to technology or culture today.

## Slide 3: 19 September 1986 – Colwich. 1 dead, 75 injured Signal Passed at Danger (SPAD)
Driver didn’t understand meaning of flashing yellow aspects, thinking the route was set all way through junction
Driver couldn’t stop in time at red signal and collided with train correctly signalled in opposite direction
Recommendations included “more attention being paid to updating the rules and other safety documentation” and to consider risks where flank protection cannot be provided
Notes: One dead, 75 injured

## Slide 4: 04 Mar 1989 – Purley. 5 dead 88 injured SPAD
Non-stopping train passed a signal at danger and ran into back of train which had just departed slow line at Purley Station, crossing over to fast line
Signal had a history of being passed at danger, with four SPADs in the previous five years
Following this On-Train Data Recorders (OTDR) were progressively introduced and it is now a requirement that all trains on Network Rail infrastructure are equipped with it
Notes: 5 dead, 88 injured

## Slide 5: 12 Jul 1991 – Newton. 4 dead 22 injured. SPAD
Two trains collided head on at single lead junction
Recent signalling alterations at Newton had replaced the existing parallel junction with a single-lead junction just a few weeks prior
Recommendations included British Rail should develop and adopt a system of risk analysis combining engineering and operating factors
Noted ATP could have prevented accident
Notes: 4 dead, 22 injured

## Slide 6: 07 Dec 1991 – Severn tunnel.185 injured – ‘False Clear’
Train moving at linespeed ran into the back of slow moving train ahead
Slow train was cautioned for an axle counter failure
Recovery operations were compounded by a lack of effective communication
Recommendations included improvements to emergency equipment and procedures but also included changes to the resetting and restoration arrangements for axle counters
Notes: 185 injured

## Slide 7: 15 October 1994 – Cowden. 5 dead 13 injured. SPAD
Driver had “disregarded” the signal and passed it at danger
Signaller was aware but unable to stop the train
Concern raised regarding the luminosity of the signal aspect, … the signal lens was found to be discoloured by insect deposits
Recommendations included checking work, monitoring standards and also full implementation of Cab Secure Radio (CSR) and improvements to the National Radio Network (NRN)
Notes: 5 dead, 13 injured

## Slide 8: 31 Jan 1995 – Ais Gill. 1 dead 30 injured. Earth works
Minor accident at first. First train derailed after running into landslide and fouled adjacent line.
Second train then collided with first.
Owing to a lack of adequate training and equipment, no emergency call was made to the driver of this second train. As a result, it struck the derailed train, killing its conductor.
Resulted in improved communication and emergency procedures
Notes: 1 dead, 30 injured

## Slide 9: 08 August 1996 – Watford. 1 dead 69 injured. SPAD
Passenger train struck by empty coaching stock (ECS)
The ECS driver failed to react to two cautionary aspects, and had ‘disregarded’ the approaching WJ759 signal at danger, possibly in anticipation of it clearing on approach as consistent with previous experience.
Recommendations relating to risk assessment of locations with reduced overlaps, better understanding the location-specific risk of SPADs and the development of a SPAD management programme
Notes: 1 dead, 69 injured

## Slide 10: 19 Sep 1997 – Southall. 7 dead 139 injured SPAD
HST passed a signal (SN254) at danger at line speed (125 mph) and ran into a freight train that had been signalled across Southall East Junction
Primary cause of the accident was the driver’s failure to respond to the two previous warning signals.
Drivers had become increasingly reliant on Automatic Warning System (AWS) which was inoperative in this instance
Major contributor to introduction of TPWS and rules regarding driving trains with defective apparatus
Notes: 7 dead, 139 injured

## Slide 11: 05 Oct 1999 – Ladbroke Grove. 31 dead 520 injured. SPAD
A Thames Trains passenger service passed a signal (SN109) at danger at Ladbroke Grove and collided head on with a Great Western HST passenger train at a combined estimated speed of around 130 mph
SN109 had a significant SPAD history
Recommendations included standards setting, accident investigation and regulation. Functions were then separated, on the model of the aviation industry
Robust signal sighting process and training implemented afterwards
Notes: 31 dead, 520 injured

## Slide 12: 17 Oct 2000 – Hatfield. 4 dead 70 injured. - Broken Rail
A rail with gauge corner cracking (GCC) caused multiple cracks and fractures, then fragmented as a high-speed train passed over it
Train derailed at 115mph.
Introduction of Plain Line Pattern Recognition (PLPR) and ultrasonics, combined with eddy current testing, to capture more accurate picture of the condition of rail in situ.
Development of a national database to record the state of all track.
Review of the recruitment and training programmes by the contractor
Notes: 4 dead, 70 injured

## Slide 13: 10 May 2002 – Potters Bar. 7 dead 76 injured. Points failure.
Points had moved underneath the train after nuts holding the stretcher bars became loose or were missing and were poorly maintained.
Recommendations included a review of the design and safety analysis of points, a review of the suitability of the standards relating to the inspection and the maintenance of points.
Minister of Transport created Network Rail to replace the originally private company Railtrack and took maintenance back in-house
Notes: 7 dead, 76 injured

## Slide 14: 06 Nov 2004 – Ufton Nervet. 7 dead 90 injuries Level Crossing user
A car was deliberately driven onto the level crossing by a suicidal motorist.
Leading wheelset of the train derailed and started to turn towards a loop line, causing the train’s leading vehicles to overturn.
Recommendations included improvements to industry’s level crossing risk assessment process, All Level Crossing Risk Model (ALCRM)
Notes: 7 dead, 90 injuries

## Slide 15: 23 Feb 2007 – Grayrigg. 1 dead 88 injured. Points set up
Stretcher bars that maintained the gauge of the points were defective, with one of the three bars not in position and nuts and bolts missing on the others.
Limited access times for maintenance of the West Coast Main Line (WCML) at Grayrigg.
Network Rail has since modified the design of non-adjustable stretcher bars
Introduction of training to install and maintain both Fixed & Adjustable Stretcher Bars
Notes: 1 dead, 88 injured