## Slide 1: Learning from history: Clapham Rail Disaster
A chance to reflect, remember and continue to learn

## Slide 2: Great Britain's Railway
1.7 billion passenger journeys - every year.
22,500 train movements– every day.
In fact Britain's railway is currently the safest in Europe for its passengers. Our railway had its last passenger accident fatality nearly 12 years ago.
We now have a generation of railway employees without that experience.
And for those with the memories, time can erode the lessons learned from major accidents.
12 December 2018 marks 30 years since a watershed moment in railway history. Clapham
Todays session
  Introducing opportunity to learn from history
  Reflect on Clapham
  Chance to learn from one or two other historic accidents
  What you can contribute in keeping the railway safe?

## Slide 3: Message from Andrew Haines chief executive.

## Slide 4: Film feedback
This may have been the first time you have heard from our new chief executive.
Discuss the main messages you picked up from Andrew Haines?

## Slide 5: Key Points
30 years since Clapham Junction
Over a decade since our last passenger fatality due to an accident on a train service.
A fantastic record.
Also a risk of complacency and to lose site of day to day risks.
Take this opportunity think and talk about acceptance of safety standards that we shouldn't be.
The recent workforce fatalities have given us a jolt.
December 2018 gives us a chance to reflect, remember and continue to learn.
Clapham Junction.

## Slide 6: Clapham Disaster
12 December 1988

## Slide 7
30 years ago at approx. 0810 on 12 December 1988. 35 people lost their lives.
The Clapham Rail Disaster shocked the whole country…

## Slide 8: On that day
3 train services-
Basingstoke - London Waterloo
Poole- London Waterloo
Empty train stock out of Waterloo
The Basingstoke service stopped at a red signal outside Clapham…
… the Poole service passed through a signal incorrectly showing Green…

## Slide 9: …and collided with the stationary Basingstoke service.

## Slide 10: The wreckage was then hit by the empty stock travelling on an adjacent line.

## Slide 11: On that day
35 people died
484 people were hurt

## Slide 12: Why did it happen?
The accident was a wrong side failure, caused by a signal failure from a simple wiring error, which occurred during installation of new re-signalling work wiring in a relay room.
What is a wrong side failure?
Why it happened ‘Immediate causes’:
Poor installation practice – not cutting back and insulating wires
Wiring error – not disconnecting redundant wires
Poor supervision of work
Defective testing – no wire count
Whilst these were the immediate causes, as in all accidents, near misses and close calls there were OTHER /CONTRIBUTING FACTORS. What could these have been?

## Slide 13: Think Where Safety Starts - Swiss Cheese
Holes are failures that cause safeguards to fail – e.g. human errors or breakdown of equipment.
Underlying causes are in the system or organisation that lead to failures.

## Slide 14: Clapham- Other factors
The enquiry determined some extremely damning failures within British Rail (BR) falling under these broad categories.
Poor safety culture existed
Lack of supervision
Staff were overworked and fatigued
Time pressures
Re-signalling project was badly planned
Inappropriate habits and working practices
Insufficient training
Issues with recruitment of competent staff

## Slide 16: ‘Hidden’ report –Recommendations Sir Anthony Hidden QC was brought in to chair the subsequent inquiry.
The report made 93 recommendations, focused on:
Recommendations to address the immediate causes of the accident
Recommendations to address the underlying causes within management
Recommendations to improve safety culture

## Slide 17: ‘Hidden’ report –Recommendations Sir Anthony Hidden QC was brought in to chair the subsequent inquiry.
The report made 93 recommendations, including:
Recommendations to address the immediate causes of the accident
  Design, installation and testing practices; instructions; training
Recommendations to address the underlying causes within Management
  Effective organisation; recruitment and retention; management of staff; safety monitoring; project management; quality management
Recommendations to improve safety culture
  Total Quality Management; external review and audit; cab radios; Automatic Train Protection; funding; reporting of signal failures; installation procedures

## Slide 18: Corporate Learning
Clapham was a turning point in the history of the railway. Many recommendations from ‘Hidden’ were made and improvements have followed. However…
The Rail Accident Investigation Branch(RAIB) recently published reports-
2017 - Cardiff Central, December 2016
2018 - London Waterloo, August 2017
And published comparisons showed that some of the lessons from the Clapham Junction accident appeared to have been forgotten.

## Slide 19: RAIB Comparisons at Clapham Junction, Cardiff and Waterloo
Clapham 1988 | Waterloo 2017 | Cardiff 2016
Working practices were permitted to slip to unacceptable and dangerous standards. | Documented processes not used. | Group culture leading to insular thinking about operational risk.
Full documentation was not available. | Out of date drawings. | Individual signalling stage schemes plans had not been produced.
The quality of testing did not meet standards set by BR. | Testing led changeover process not followed. | …was non-compliant with the standards governing the commissioning of signalling equipment.
There was no effective control over the Design Office to ensure that the workforce were supplied with drawings which accurately reflected the work to be done. | The effect of the interlocking design changes on the test desk was not apparent because the spur wires were not recorded on the interlocking detailed design documents. | There was no single project document with a complete list of all the points that required securing.
Failure to communicate effectively both up and down the lines of management. | Testers were aware, shortly before commissioning, that the test desk might not function correctly, but the necessary management actions were not communicated to relevant staff. | People who attended the briefing said that they had difficulty filtering out the information that was relevant to them as there was so much detail.
BR shall ensure that overtime is monitored so that no individual is working excessive levels. BR, in conjunction with the Unions, shall introduce the concept of scheduled hours in order to make better provision for work which has to be carried out at weekends. |  | The project team had signed up to a fatigue management agreement but it was not reliably implemented.

## Slide 20: Do we learn lessons?
Clapham was just one of a number of catastrophic accidents in the 80’s and 90’s.
We must not forget these incidents, we must learn and we must follow the rules, standards and procedures that are in place.

## Slide 21: Optional
Facilitator to add one or two local historical lesson…
This could be relevant to work, geography, recent incident or local expertise
See appendix slides sent with pack to insert information relevant to session
Appendix A – Other Significant passenger accident learning
Appendix B – Fatigue Improvement Programme
Appendix C - Drugs and Alcohol

## Slide 22: Andrew Haines- Closing Message.
Insert/play Andrew Haines closing film.

## Slide 23
At the beginning of the session we asked you to consider one question
What you can contribute in keeping the railway safe (for passengers, workforce, yourself)?

## Slide 24: Closing.
The railway and its systems are fundamentally no different from 30 years ago, and the safety we enjoy has been earned.
However, it is solely dependent on people to maintain that safety.
People like you.
"Those who cannot remember the past are condemned to repeat it”
George Santayana- Philosopher
Clapham Memorial