## Slide 1
KEY
Minimising exposure (more to the left if many people or longer timescales)
PPE
Engineering controls
Substitution
Elimination
Through good planning, machine and plant selection and risk based maintenance, the amount of ballast moving can be reduced
Can manual ballast moving activity be eliminated?
Or can dust created by machinery be eliminated?
Guide for Ballast Dust
Risk
Shall be implemented
Shall be considered and done if reasonably practicable
Segregation barriers
Admin controls
All persons briefed on risk of ballast dust and trained in use of control measures
Automated water suppression
Occupational health surveillance in place for all those exposed to risk, mandatory attendance by employees
Clean storage for RPE provided and maintain equipment in accordance with guidelines
Can ballast be replaced with other suitable (non-silica) based foundation?
Good hygiene to avoid ingestion – suitable washing, reduced smoking, eating and drinking areas
Staff undertake respiratory e-leaning
Personal exposure monitoring
Manual water suppression
Filtering facepiece (FFP3) with assigned protection factor (AFP) of 20
Change filters on respirators in accordance with manufacturers proposals
Wear eye protection – grade B
Force ventilation
Face fit testing must be conducted prior to undertaking task
Dust warning mechanisms
Static exposure monitoring
Standard compliance and assurance through audit, inspection, supervision, PAISS
Manual operations
<2M from source or if wind could cause exposure
<1HR EXPOSURE and less than three people in open environment
Scenario 1
Tight fitting disposable mask
*Wet conditions may reduce the risk further however, minimum mitigations remain the same

## Slide 2
KEY
Minimising exposure (more to the left if many people or longer timescales)
PPE
Engineering controls
Substitution
Elimination
Through good planning, machine and plant selection and risk based maintenance, the amount of ballast moving can be reduced
Can manual ballast moving activity be eliminated?
Or can dust created by machinery be eliminated?
Guide for Ballast Dust
Risk
Shall be implemented
Shall be considered and done if reasonably practicable
Segregation barriers
Admin controls
All persons briefed on risk of ballast dust and trained in use of control measures
Automated water suppression
Occupational health surveillance in place for all those exposed to risk, mandatory attendance by employees
Clean storage for RPE provided and maintain equipment in accordance with guidelines
Can ballast be replaced with other suitable (non-silica) based foundation?
Good hygiene to avoid ingestion – suitable washing, reduced smoking, eating and drinking areas
Staff undertake respiratory e-learning
Personal exposure monitoring
Manual water suppression unless ballast is heavily wet due to weather conditions
Maintenance and filter changes in accordance with manufacturers guidance and must be documented.
Powered air respirator required with integral visor. FFP3 APF20
Wear eye protection – GRADE B
Forced ventilation
Dust warning mechanisms
Static exposure monitoring
Standard compliance and assurance through audit, inspection, supervision, PAISS
Manual operations
<2m from source or if wind could cause exposure
>1HR EXPOSURE or/and more two people
Scenario 2
*Wet conditions may reduce the risk further however, minimum mitigations remain the same

## Slide 3
KEY
Minimising exposure (more to the left if many people or longer timescales)
PPE
Engineering controls
Substitution
Elimination
Through good planning, machine and plant selection and risk based maintenance, the amount of ballast moving can be reduced
Can ballast moving activity be eliminated?
Or can dust created by machinery be eliminated?
Guide for Ballast Dust
Risk Control
Shall be implemented
Shall be considered and done if reasonably practicable
Exclusion zones in place
Admin controls
All persons briefed on risk of ballast dust and trained in use of control measures
Occupational health surveillance in place for all those exposed to risk, mandatory attendance by employees
Clean storage for RPE provided and maintain equipment in accordance with guidelines
Can ballast be replaced with other suitable (non-silica) based foundation?
Good hygiene to avoid ingestion – suitable washing, reduced smoking, eating and drinking areas
Staff undertake respiratory e-leaning
Personal exposure monitoring
Maintenance and filter changes in accordance with manufacturers guidance and must be documented.
Powered air respirator required with integral visor. FFP3 APF20
Wear eye protection – GRADE B
Forced ventilation
Face fit testing must be conducted for tight fitting face mask
Dust warning mechanisms
Static exposure monitoring
Standard compliance and assurance through audit, inspection, supervision, PAISS
Mechanical operations *DRY CONDITIONS
<10m from source or if wind could cause exposure
Scenario 3
Protected OTP in cabs with forced air and HEPA filters
Automated water suppression or if not possible then manual water suppression – consider damping at source
Tight fitting FFP3 where exposure is less than 1hour
Vehicle windows to be closed at all times
*Wet conditions may reduce the risk further however, minimum mitigations remain the same

## Slide 4
KEY
Minimising exposure (more to the left if many people or longer timescales)
PPE
Engineering controls
Substitution
Elimination
Through good planning, machine and plant selection and risk based maintenance, the amount of ballast moving can be reduced
Can ballast moving activity be eliminated?
Or can dust created by machinery be eliminated?
Guide for Ballast Dust
Risk Control
Shall be implemented
Shall be considered and done if reasonably practicable
Exclusion zones in place
Admin controls
All persons briefed on risk of ballast dust and trained in use of control measures
Occupational health surveillance in place for all those exposed to risk, mandatory attendance by employees
Clean storage for RPE provided and maintain equipment in accordance with guidelines
Can ballast be replaced with other suitable (non-silica) based foundation?
Good hygiene to avoid ingestion – suitable washing, reduced smoking, eating and drinking areas
Staff undertake respiratory e-leaning
Personal exposure monitoring
Change filters on respirators in accordance with manufacturers proposals
Powered respirator required with integral visor if over one hour exposure otherwise RPE with assigned protection factor of least 40 FFP3
Wear eye protection
Forced ventilation
Face fit testing must be conducted
Dust warning mechanisms
Static exposure monitoring
Standard compliance and assurance through audit, inspection, supervision, PAISS
Mechanical operations wet conditions
Less than 10m from source or if wind could cause exposure
Scenario 4
Protected OTP in cabs with forced air and filters
Automated water suppression or if not possible then manual water suppression – consider damping at source

## Slide 5
KEY
Minimising exposure (more to the left if many people or longer timescales)
PPE
Engineering controls
Substitution
Elimination
Through good planning, machine and plant selection and risk based maintenance, the amount of ballast moving can be reduced
Can ballast moving activity be eliminated?
Or can dust created by machinery be eliminated?
Guide for Ballast Dust
Risk Control
Must be implemented
Must be considered and done if reasonably practicable
Exclusion zones in place
Admin controls
All persons briefed on risk of ballast dust and trained in use of control measures
Occupational health surveillance in place for all those exposed to risk, mandatory attendance by employees
Clean storage for RPE provided and maintain equipment in accordance with guidelines
Can ballast be replaced with other suitable (non-silica) based foundation?
Good hygiene to avoid ingestion – suitable washing, reduced smoking, eating and drinking areas
Staff undertake respiratory e-leaning
Personal exposure monitoring
Maintenance and filter changes in accordance with manufacturers guidance and must be documented
Operating within exclusion zone - Powered air respirator required with integral visor. FFP3 APF20
Wear eye protection – GRADE B
Force ventilation or full risk assessment including tunnel airflow analysis
Face fit testing must be conducted
Dust warning mechanisms
Static exposure monitoring
Standard compliance and assurance through audit, inspection, supervision, PAISS
Mechanical and manual operations in TUNNEL
Applies to everyone in the tunnel
Scenario 5
Protected OTP in cabs with forced air and HEPA filters
Automated water suppression or if not possible then manual water suppression – consider damping at source
Vehicle windows to be closed at all times
Operating outside of exclusion zone - Tight fitting FFP3 for maximum of 1hour
*Wet conditions may reduce the risk further however, minimum mitigations remain the same