Road Rail Vehicle Safety Improvement Programme

3M Peltor DECT-Com II - Frequently Asked Questions

DECT-com II is a very reliable system, but good system set up is essential for most effective operation. The following answers to frequently asked questions should help in system set up ensuring on-going reliable performance:

Effective Range

Question: Reception is sometimes poor – can I resolve this?

Answer:  The range on DECT II is up to 150metres. To get best reception, the base unit cradle must be fitted above the metal chassis of the cab to improve range. This can be done using Velcro pads or other suction mechanisms to stick the cradle to the glass of the cab.

Extension cables are readily available making sure the cradle can be located as high as possible in the cab with no pull issues for the Machine Operators headset.

Coloured bands positioned below the antenna

Question: Is there any significant of the different coloured bands used?

Answer: YES. Black=Base/Portable with external connections (DC2815); Red=Base/Portable (DC2812); Green=Portable (DC2811). Only black or red should be used in the RRV cradle

Battery Life

Question: What’s battery life in operation?

Answer: The portable units have approximately 40 hours life between charges. The base unit should be put in the base unit power supply pod (DC2068) which is plugged in to the 12/24v auxiliary socket in the OTP or directly wired in to the OTP.

Question: Can I charge the HANDSET green band in the base station cradle?

Answer: No! It is a common misconception that handsets can be used in the base station cradle, particularly to increase battery life. This will not preserve battery life and MUST NOT be done. The vehicle power supply pod (DC2068) is NOT a charger.

Question: Can I use the handset charging pod (DC2064) in a RRV.

Answer: NO. If this is tried the unit will be damaged and will no longer function.

Question: If I charge the base station and handset for an hour or so, will this be sufficient to see me through my shift.

Answer: NO! Units should be charged for 12 hours before use. The biggest problem with battery life is that the 12/24v auxiliary socket is faulty, the 12/24v auxiliary socket is not used to plug the cradle into, or the equipment is not fully charged before use. The bases will only last 5 hours maximum.

In the event of jobs being 52 hours, or longer such as for long weekend working, or blockades, exchanging handsets every 24 hours eliminates battery issues on the long shift. This means ordering additional handsets from your supplier with the kit labeled e.g. KIT 1(1A,1B.1C) where handset A/B are used for the first 24 hours and then handset C/B are used for the remainder of the shift.

12v/24v socket testers can easily check if a machine has a faulty auxiliary socket.

Note that for generator powered sites, if power is removed from site, DECT kit will need to be charged away from site. It requires 12 hour to be fully charged. When finishing with DECT-com switch the equipment off as this will make it easier to operate for the on coming shift.

Headset fitting

Question: My headset doesn’t sit comfortably – what can I do?

Answer:  There is a clip on RRV TV on Network Rail’s Safety Central web site that shows how to fit these. The headsets fit most people, but not everyone, and this can result in the microphone not sitting in front of the mouth, leading to machine operators and machine controllers having to lower the VOX setting down significantly, which increases ambient noise captured. Throat mics’ offer a solution to this, eradicating ambient noise intrusion, and are suitable for most people.

When a throat mic’ is used, there are hygiene, noise reduction and the wearing of protective glasses advantages. As the microphones are tight against the user’s neck, only their voice is heard and outside noise is virtually eliminated. As there is no boom mic’, the hygiene issue with the boom mic’ is eliminated and the invisi tube earpieces are issued personal issue.

Locking out system functions

Question: Can VOX control be locked out in system set up?

Answer: If an Electret sidewinder headset or throat mic’ set is used, there is no requirement to adjust the VOX levels, as these are preset, and anyone talking on either device will activate the VOX. This simplifies system use, and substantially reduces risk of operator error.

If a noise cancelling headset is used VOX control MUST NOT be locked out. These use microphones that allow the VOX level to be set at a low level to eliminate ambient noise. The microphone has to receive audio both sides of the microphone to activate it, and this can only be done when the microphone is set very close to the operator’s mouth.

Software and Firmware upgrades

Question: Is the firmware and software on the equipment up to date?

Answer: The latest firmware release was issued on 20 June 2013. The last software upgrade was on 22 August 2012. Companies who have the capability to programme DECT II are on the manufacturer’s database and get an email advising that the latest upgrade is available on 3M Peltor Extranet.

PPT buttons

Question: Do the PTT buttons service any purpose?

Answer: For PTT 1, if auto talk is enabled this isn’t needed. If it isn’t enabled, on the hand set for conference connection press PTT1 twice to couple with the base Unit.

PTT2 is not programmed so has no functionality. PTT3 is only used for back-to-back radio capability when Motorola GP340 is connected. The need for this is very rare.

Cleaning and testing

Question: Should equipment be cleaned regularly and tested?

Answer: The DECT II units should be cleaned periodically using sanitising wipes. Headsets and throat mics’ should be cleaned after every use. Ear buds should be replaced on throat mics’ when the user changes. Everything should be tested before it is deployed.