## Slide 1: Emergency Change NR/BS/LI/413
Standard affected: NR/L2/OHS/022 Issue 1, Working Safely at Height

## Slide 2: Reason for Issue
This emergency change is required to bring NR/L2/OHS/022 Working Safely at Height in line with Work at Height Regulations regarding the use of ladders and step ladders.
The Standard applies to all “Work at Height” carried out by Network Rail employees, contractors and others working on behalf of Network Rail on Network Rail owned or managed property or infrastructure.

## Slide 3: Work At Height
“Work at Height” is defined as any work activity where there is a need to control a risk of a person or object falling a distance liable to cause personal injury.
This is regardless of the work equipment being used, the duration the person is at height or the height at which the work is being performed.
It includes access to and egress from a place of work.
Update to examples of working at height now includes:-
Activities within a building which do involve a risk of falling, e.g. window cleaning or changing a light bulb from a step-ladder, would be considered to be work at height.

## Slide 4: Changes
Clause 14.1 General Requirements – Portable ladders and step ladders
Portable ladders and step ladders used for access and egress to work areas shall be BS EN 131 Professional Use or Class 1 BS 2037/1129 Heavy Industrial use (not to be confused with EN 131 Light Industrial use).
NOTE 1: Ladders certified to the withdrawn British Standards, BS 2037 and BS 1129 (often referred to as Class 1 ladders) will no longer be available (to purchase) after a transition period but can still be used.
NOTE 2: When ladders are deployed on ballast, a suitable additional anchorage device should be used to prevent slippage (e.g. ratchet strap secured to the rail or fixed structure).

## Slide 5: Changes
Clause 14.2 Assessment and use of portable ladders and step ladders
This clause has been completely rewritten for the use of portable ladders and step ladders.
A portable ladder or step ladder may only be used for work at height if a risk assessment under regulation 3 of the Management Regulations has demonstrated that the use of more suitable work equipment is not justified because of the low risk and:
a) the short duration of use (maximum of 30 minutes); or
b) existing features on site which cannot be altered.
This assessment can be completed by following the Work Activity Risk Assessment Process detailed in NR/L2/OHS/00102 Work
Activity Risk Assessment.
Full details on Emergency Change Document

## Slide 6: Changes
Clause 14.3 Fixed Ladders
Whenever a fixed ladder is climbed the person climbing the ladder
shall always carry out a visual check of the structure and ladder,
particularly the securing points, both prior to climbing and as they
climb the structure.
If the climber has any doubt that the ladders are
safe to climb, they shall not climb them until they are made safe.
The user shall not carry any load up a fixed ladder. Suitable means
of carrying loads must be provided, such as tool belts.